| SECTION 09510 / 09 51 00 USG TRUE WOOD LAY IN AND ACCESSIBLE REVEAL WOOD CEILING PANELS |  | Product Specification |
| --- | --- | --- |

Copyright 1997, The American Institute of Architects (AIA)

This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

REFERENCES

ASTM C635, Standard Specifications for Metal Suspension Systems

ASTM C636, Recommended Practice for Installation of Metal Suspension System

ATSM E84, Standard Test Method for Surface Burning Characteristics of Building Materials

CISCA Ceiling Systems Installation Handbook.

CISCA Wood Ceilings Technical Guidelines

SUMMARY

Section Includes:

Acoustical ceilings panels

Exposed grid suspension system.

Wire hangers, fasteners, main runners, cross tees, and wall angle moldings.

Related Sections include the following:

Section 01 41 13 (01450) - Codes

Section 01 45 33 (01450) - Code-required Special Inspections and Procedures

Section 09 20 00 (09250) - Plaster and Gypsum Board

Divisions 23 (15) - HVAC

Division 26 (16) Sections - Electrical Work

List below only products that the reader might expect to find in this Section but are specified elsewhere.

SUBMITTALS

Samples: Submit panel finish and suspension system main and cross tees for acceptance.

Shop drawings:

Reflected ceiling plans: Submit ceiling suspension system layout indicating dimensions, lighting fixture locations, and related mechanical components.

Assembly drawings: Indicate installation details, accessory attachments and installation of related lighting fixtures and related mechanical system components.

Samples: Minimum 4 inch x 6 inch samples of specified acoustical panel; 8 inch long samples of exposed wall molding and suspension system, including main runner and 4 foot cross tees.

Manufacturer’s data:

System details: Submit manufacturer’s catalog cuts, literature, or standard drawings showing details of system with project conditions clearly identified and manufacturer’s recommended installation instructions.

Maintenance materials: Provide _____ % of amount of main tees, cross tees, and panels.

DELIVERY, STORAGE, AND HANDLING

Delivery of materials: Deliver materials in original unopened packages, clearly labeled with manufacturer’s name, item description, specification number, type, and class as applicable.

Inspection: Promptly inspect delivered materials, file freight claims for damage during shipment, and order replacement materials as required. Any damaged materials shall be promptly removed from the job site.

Storage: Store in manner that will prevent warpage, water damage, or damage of any kind. Prevent interference to/by other trades and any other adverse job conditions due to storage locations or methods.

Handling: Handle in such a manner as to ensure against racking, distortion, or physical damage of any kind.

Retain subparagraphs below to suit Project or insert others.

QUALITY ASSURANCE

Subcontractor qualifications: Installer shall have not less than three years of successful experience in the installation of ceiling suspension systems on projects with requirements similar to requirements specified.

Requirements of regulatory agencies: Codes and regulations of authorities having jurisdiction.

Delete paragraph below if not required.  If retaining, indicate location, size, and other details of mockups on Drawings or by inserts.  Revise wording if only one mockup is required.

Source quality control: Manufacturer will provide test certification for ceiling system as required to meet industry performance standards specified by various agencies.

Delete below if work of this Section is not extensive or complex enough to justify a preinstallation conference.  If retaining, coordinate with Division 1 Section "Project Meetings."

Pre-installation Conference:  Conduct conference at Project site to comply with requirements in Division 1 Section "Project Meetings."

PROJECT CONDITIONS

Retain below for interior installations.

Building conditions:  Building shall be enclosed with all windows and exterior doors in place and glazed, and the roof watertight before installation of suspension system.

Interior temperature/humidity in building:  Climatic conditions in areas to receive ceiling suspension systems shall range from 60°F (16°C) to 85°F (29°C) and relative humidity of not more than 55% shall be maintained before installation of components.

EXTRA MATERIALS

Furnish extra materials described below that match products installed and that are packaged with protective covering for storage and identified with labels describing contents.

Ceiling Panels: Furnish quantity of full-size units equal to ___ % of amount installed.

Extra materials may not be allowed for publicly funded projects.

PRODUCTS

PRODUCTS AND MANUFACTURERS

In lieu of using schedule at the end of Part 3, insert names of products and manufacturers and revise paragraph above or below to suit Project.

USG TRUE WOOD ceiling panels and DONN Brand suspension systems as manufactured by USG Interiors, Inc., Chicago, Illinois, U.S.A.

MATERIALS

USG TRUE WOOD ceiling panels:

PART 1 - USG TRUE WOOD ceiling panels will be made with a [veneer species] face veneer, [veneer cut] [veneer match], applied to a 3/4” thick core material. The edge treatment on the Wood Square panels shall be the [selected style].  The standard TRUE WOOD ceiling panel shall be 3/4" thick and [selected size] (nominal). Wood is a natural product that will undergo changes with variations in the environment. Therefore, all dimension tolerances shall be ± 1/8".

Accessories:

M9 wall molding: 15/16”x9/16”x12’ -long angle shape of prepainted steel.

In lieu of using schedule at the end of Part 3, delete paragraph below and insert product characteristics.

METAL SUSPENSION SYSTEMS

DONN Brand Suspension Systems – Commercial quality, cold-rolled steel, hot-dipped galvanized steel body. Materials Exposed surfaces color: coordinate with color of selected ceiling panels. Edge trim: Optional; COMPÄSSO [selected size]

- [DONN Brand DX 15/16” suspension System]

  - Main Tee : DX/DXL26, 12 ft x 1.64 in Heavy Duty Fire-Rated

  - Cross Tee: DX/DXL424, 4 ft x 1-1/2 in

  - Cross Tee: DX/DXL216, 2 ft x 1 in (for 2’ x 2’ only)

- [DONN Brand Fineline DXF/DXLF Ceiling Suspension System]

  - Main Tee: DXFH2924, 12 ft Main Tee Notch 24 in on center

  - Cross Tee: DXF429, 4 ft Cross Tee ( 2’ x 4’ only)

  - Cross Tee: DXF429N, 4 ft Cross Tee Notched mid-point (2’ x 2’ only)

  - Cross Tee: DXF229, 2 ft Cross Tee (2’ x 2’ only)

- [DONN Brand Centricitee DXT/DXLT Ceiling Suspension System]

  - Main Tee: DXT26, 12 ft x 1.64 in Heavy Duty

  - Cross Tee: DXT424, 4 ft x 1-1/2

  - Cross Tee: DXT222, 2 ft x 1-1/2 (2’ x 2’ only)

Suspension system:  designed to support ceiling assembly as indicated on project drawing with maximum deflection of 1/360.

EXECUTION

EXAMINATION

Examine substrates and structural framing to which ceiling systems attach or abut, with Installer present, for compliance with requirements specified in this and other Sections that affect ceiling installation and anchorage, and other conditions affecting performance of ceiling systems.

Proceed with installation only after unsatisfactory conditions have been corrected.

Work to be concealed:  Verify work above ceiling system is complete and installed in manner that will not affect layout and installation of system components.

PREPARATION

Edit paragraph below to suit Project.

Coordination: Furnish layouts for cast-in-place anchors, clips, and other ceiling anchors whose installation is specified in other Sections.

Measure each ceiling area and establish layout of 3-dimensional ceiling systems. Comply with layout shown on reflected ceiling plans.

Field dimensions:  Installer must verify actual field dimensions prior to installation.

Delete subparagraph below if not required.

INSTALLATION

Ceiling Framing:

Standard reference: Install grid members in accordance with ASTM C636, CISCA installation standards, and other applicable references.

Manufacturer’s reference: Install in accordance with manufacturer’s current printed recommendations.

Drawing reference: Install in accordance with approved shop drawings and locate ceiling in accordance with main tee dimensions relative to elevations.

Hanger Wire Installation: Secure hanger wires to upper structural elements and space hangers so that each hanger wire supports a maximum of 16 sq. ft.

Space main tee members a maximum span of 48” on center. Space cross tees to achieve a 2’ x 2’ grid for 2’ x 2’ panels or 4’ x 4’ grid for 4’ x 4’ panels.

Ceiling Panels

Preparation:  Remove dirt and debris from surrounding area.  Comply with manufacturer’s written instructions.

Install ceiling panels in accordance with approved shop drawings.

CLEANING

Suspension system:  Remove infill material and perform any necessary cleaning maintenance with non-solvent based commercial cleaner.

Touch up all minor scratches and spots, as acceptable, or replace damaged sections when touch up is not permitted.

Painting:  Repainting of suspension members shall be with a high-quality solvent base paint and applied as recommended by paint manufacturer.

Removal of debris:  Remove all debris resulting from work of this section.

Clean exposed surfaces of ceiling systems. Comply with manufacturer’s written instructions for cleaning and touchup of minor finish damage. Remove and replace ceiling system components that cannot be successfully cleaned and repaired to permanently eliminate evidence of damage, including dented and deformed members.

Safety First!

Follow good safety and industrial hygiene practices during handling and installing of all products and systems. Take necessary precautions and wear the appropriate personal protective equipment as needed. Read material safety data sheets and related literature on products before specification and/or installation.

END OF SECTION 09510
**************************************************************************
The text material contained herein is intended for use as product reference material by architects, engineers, other design professionals, contractors, building code officials, or other competent construction industry trade factors having an interest in the selection, specification and use of products manufactured by the subsidiaries of USG Corporation. It is intended solely as technical support incident to the sale and use of our products.

These materials may be printed and/or transferred electronically as needed by the user. Modification of this information is the sole responsibility of the Design Professional. Any unauthorized duplication or reuse of the material contained herein is a violation of law.

**************************************************************************